## Slide 1
Practical Quantum Communication:
From Lab to Real-World Applications
Md Mehdi Hassan
Quantum Research Fellow
Nasdaq

## Slide 2
Outline: Today
Quantum Communication in HFT
Experimental Implementation:
- NV Center in Diamond
Recap: Last Week
Quantum Network
Quantum Clock Synchronization

## Slide 3
High-Frequency Trading
Overcoming the delay obstacle using quantum technology
CHSH Game analogy:
3 min*
they choose the same color when at least one player receives Head
they choose different color when both receives Tail

## Slide 4
High-Frequency Trading
Overcoming the delay obstacle using quantum technology
CHSH Game analogy:
3 min*
they choose the same color when at least one player receives Head
they choose different color when both receives Tail

## Slide 5
High-Frequency Trading
Overcoming the delay obstacle using quantum technology
CHSH Game analogy:
3 min*
Success Probability ≈ 0.8536

## Slide 6
High-Frequency Trading
Overcoming the delay obstacle using quantum technology
56.3 km
187.8 μs (Physical Limit)
THE MARKET REALITY
200 microseconds sounds impressive, but stock prices change even faster.
Notes: Suppose you have some stock in Nasdaq and some in NYSE. The stock prices are correlated. For example, the stock price of oil (ExxonMobil (NYSE: XOM) ) and the stock price of airlines (United Airlines (NASDAQ: UAL)); An increase in oil prices may benefit ExxonMobil while increasing fuel costs for United Airlines, so they are anti-correlated.

## Slide 7
CHSH Game- Toy Model
Overcoming the delay obstacle using quantum technology
Notes: Your strategy might me if the oil price tends to go up, you immediately want to buy some oil stock and to sell some Airline stocks.
But if you want to wait 200 microsec, the price may have already changed in an unfavorable way.
You want a strategy for Tacit Coordination
Can Quantum Mechanics help you in this scenario?

## Slide 8
CHSH Game- Toy Model
Overcoming the delay obstacle using quantum technology
:: Utility Matrix ::

## Slide 9
CHSH Game- Toy Model
Overcoming the delay obstacle using quantum technology
:: Utility Matrix ::
Notes: Here, instead of Head=0, Tail=1, we say Indicator=0, no-indicator=1

## Slide 10
High-Frequency Trading
Overcoming the delay obstacle using quantum technology
probability p : the indicator I is observed
Credit: http://arxiv.org/abs/2407.21723

## Slide 11
Experimental Implementation
CHSH Game -> Bell Test
Using
NV Center in Diamond

## Slide 12
Bell Test: Variation
Loophole-Free Bell Test
Defect Qubit
(XV Center)
Photonic
Superconducting
Qubit
Polarization
Time-bin

## Slide 13
Loophole-Free Bell Test
(Using NV Center in Diamond)
Credit: http://arxiv.org/abs/1212.6136

## Slide 14
Loophole-Free Bell Test
(Using NV Center in Diamond)
Outline
How NV Center in Diamond is Created
What version of NV is desired
How to achieve that version
What hardware would be necessary?

## Slide 15
NV Center Electronic Structure
1. How NV center is created:
Notes: Kick out one carbon in the middle
Replace another neighbor carbon with Nitrogen -> You got NV center
This is NV(0). Sometimes from the defects of neighboring NV-0 center, an electron escape and join to the system of interest.
It makes NV(-) system

## Slide 16
NV- is preferable since it gives you at least two spin state
ms=0 and ms =-1
2. What version of NV center is desired:

## Slide 17
Prepare NV⁻ instead of NV⁰
Once NV⁻ is present, optically pump its ground-state spin predominantly into ms=0
3. How to achieve NV- state:
Notes: Goal is to make NV(-) state probability higher than NV(0).
Aper preparing, there is a readout process to verify if it was really in NV(-) state or not

## Slide 18
NV Center Electronic Structure
3. How to achieve NV- state:
Notes: ^4A_2: electron-electron interactions
Since S=1 here in NV(-), there would be m_s = -1, 0, +1 spin states is spin triplet state, and S=0 in spin singlet state m_s = 0
m_s = 0 of triplet state and m_s = 0 from singlet state are different in the energy level.

## Slide 19
NV Center Electronic Structure
*Not universal
The local defect electric field dictates the gap
Selection Engineering
* Which Ground State to choose?
3. How to achieve NV- state:
Notes: You can apply external static electric field to mess up with the system and it will let you control the energy gap between ground and exited states.

## Slide 20
NV Center Electronic Structure
Selection Engineering
*How to choose a particular state?
3. How to achieve NV- state:
Zero-field Splitting
(Spin-Spin interaction)
Notes: By applying static magnetic field, you can split the energy level between m_s=-1 and m_s =+1 via Zeeman effect.

## Slide 21
3. How to achieve NV- state:
*Apply laser pulses with 535 nm wavelength
- Where does it go?
Notes: ^4A_2: electron-electron interactions

## Slide 22
3. How to achieve NV- state:
*Apply laser pulses with 535 nm wavelength
- Goes above and then decays back or goes to another site
³E
³A₂
Non-Radiative
Decay
Off-Resonant
Excitation
637-800 nm
Phonon-Sideband
Fluorescence
Zero-Phonon
Line
(637 nm)
Notes: ^4A_2: electron-electron interactions

## Slide 23
4. Hardware requirements:
*Apply laser pulses with 535 nm wavelength
- Where does it go?
2 μs pulse at approximately 400 μW
During optical cycling, electrons can transfer from nearby donors or traps to NV⁰, producing NV⁻
Notes: ^4A_2: electron-electron interactions

## Slide 24
# How to verify NV- state?
-> Using ZPL line: 637 nm or 575 nm? Using green laser.
# How long it will remain over there?
-> There is no single fixed lifetime. In the dark, NV⁻ can remain stable for a long time, but optical illumination can photoionize it into NV⁰
# How to select m_s=0 state in NV- system?
->532 nm Laser, 1-5 micro-sec pulse, at 100 micro-watt power
Notes: ^4A_2: electron-electron interactions

## Slide 25
To generate a photon entangled with the spin state |0>: 3E -> 3A2
3.1 How to achieve NV- state
with ms = 0:
Notes: ^4A_2: electron-electron interactions

## Slide 26
To generate a photon entangled with the spin state |0>: 3E -> 3A2
The resonant wavelength would be 637 nm (ZPL).
How to excite it from the ground state to the excited state?
?
3.1 How to achieve NV- state
with ms = 0:
Notes: ^4A_2: electron-electron interactions

## Slide 27
What about this one?
3.1 How to achieve NV- state
with ms = 0:
Notes: 2.87 GHz in microwave frequency level.

## Slide 28
-How to achieve NV- state:
What about this one?
- Non-radiative decay (phonon/heat)
Notes: ^4A_2: electron-electron interactions

## Slide 29
To generate a photon entangled with the spin state |0>: 3E -> 3A2
The resonant wavelength would be 637 nm.
How to excite it from the ground state to the excited state?
-How to achieve NV- state:
Notes: ^4A_2: electron-electron interactions

## Slide 30
Loophole-Free Bell Test
(Using NV Center in Diamond)
NV Center Electronic Structure
Selection Engineering
?
Notes: A resonant \pi/2 microwave pulse rotates the NV spin from m_s=0 into an equal coherent superposition of m_s=0 and m_s=-1

## Slide 31
Loophole-Free Bell Test
(Using NV Center in Diamond)
Starting from state |0>:
Notes: ^4A_2: electron-electron interactions

## Slide 32
Selection Engineering:
What wavelength to choose?
# The rotation would be about Y axis
# π/2 rotation ->
# The cycling of population between
the two states is denoted as
“Rabi oscillation”
Notes: ^4A_2: electron-electron interactions

## Slide 33
Selection Engineering:
What wavelength to choose?
Notes: ^4A_2: electron-electron interactions